## Slide 1: b1010 Assembly
ENGR xD52
Eric VanWyk
Fall 2012

## Slide 2: Today
Context of Assembly
Your First Assembly Programs

## Slide 3: What is Assembly?
Assembly is the lowest level language that humans routinely deal with
Simple, regular instructions
  building blocks of C & other languages
One-to-one mapping to machine language
  … Usually

## Slide 4: What is Assembly?
It is how we feed steps 1 & 2
Instruction
Fetch
Instruction
Decode
Operand
Fetch
Execute
Result
Store
Next
Instruction

## Slide 5: Why Shouldn’t I learn Assembly?
Writing in Assembly is usually slower than writing in other languages
  Time to Market!
Assembly is not portable
  Specific to a processor
Modern Compilers are pretty darn good

## Slide 6: Why Should I Learn Assembly?
Someone has to write those compilers…
Hand Optimized Assembly can be wicked fast
Reading Assembly >>> Writing Assembly
Good practice for designing VMs/protocols
Initializing an embedded system
  Setting up Memory, Transitioning execution…

## Slide 7: Why Should I learn Assembly?
It will make you a better software architect
Optimize from the top down

## Slide 8: How should I learn Assembly?
Generically!
With a cheat sheet in hand
Do Not Memorize Specifics

## Slide 9: “C is Built On Assembly”
WRONG
C is built on Machine Code
Machine Code can be decompiled to Assembly
Assembly -> Machine Code -> Assembly loses relatively little information

## Slide 10: MIPS Assembly Language
The basic instructions have four components:
  Operator name
  Destination
  1st operand
  2nd operand
add <dst>, <src1>, <src2> # <dst> = <src1> + <src2>
sub <dst>, <src1>, <src2> # <dst> = <src1> - <src2>
Simple format: easy to implement in hardware
More complex: A = B + C + D – E

## Slide 11: Register File Allocation
Register | Name | Function | Comment
$0 | $zero | Always 0 | No-op on write
$1 | $at | Reserved for assembler | Don’t use it!
$2-3 | $v0-v1 | Function return | 
$4-7 | $a0-a3 | Function call parameters | 
$8-15 | $t0-t7 | Volatile temporaries | Not saved on call
$16-23 | $s0-s7 | Temporaries (saved across calls) | Saved on call
$24-25 | $t8-t9 | Volatile temporaries | Not saved on call
$26-27 | $k0-k1 | Reserved kernel/OS | Don’t use them
$28 | $gp | Pointer to global data area | 
$29 | $sp | Stack pointer | 
$30 | $fp | Frame pointer | 
$31 | $ra | Function return address | 

## Slide 12: Register File Allocation
STOP MEMORIZING THIS
Register | Name | Function | Comment
$0 | $zero | Always 0 | No-op on write
$1 | $at | Reserved for assembler | Don’t use it!
$2-3 | $v0-v1 | Function return | 
$4-7 | $a0-a3 | Function call parameters | 
$8-15 | $t0-t7 | Volatile temporaries | Not saved on call
$16-23 | $s0-s7 | Temporaries (saved across calls) | Saved on call
$24-25 | $t8-t9 | Volatile temporaries | Not saved on call
$26-27 | $k0-k1 | Reserved kernel/OS | Don’t use them
$28 | $gp | Pointer to global data area | 
$29 | $sp | Stack pointer | 
$30 | $fp | Frame pointer | 
$31 | $ra | Function return address | 

## Slide 13: Register File Allocation Redux
0 is $zero is 0x00000000
  The only physically special address
  Specific to MIPS!
The other 31 are all interchangeable
But we treat them differently for convenience
For today, we’ll use $t0 through $t9

## Slide 14: Basic Operations
Mathematic: add, sub, mult, div add $t0, $t1, $t2 # t0 = t1+t2
Unsigned (changes overflow condition) addu $t0, $t1, $t2 # t0 = t1+t2
Immediate (one input a constant) addi $t0, $t1, 100 # t0 = t1+100
Logical: and, or, nor, xor and $t0, $t1, $t2 # t0 = t1&t2
Immediate andi $t0, $t1, 7 # t0 = t1&b0111
Shift: left & right logical, arithmetic sllv $t0, $t1, $t2 # t0 = t1<<t2
Immediate sll $t0, $t1, 6 # t0 = t1<<6

## Slide 15: Basic Operations
Mathematic: add, sub, mult, div add $t0, $t1, $t2 # t0 = t1+t2
Unsigned (changes overflow condition) addu $t0, $t1, $t2 # t0 = t1+t2
Immediate (one input a constant) addi $t0, $t1, 100 # t0 = t1+100
Logical: and, or, nor, xor and $t0, $t1, $t2 # t0 = t1&t2
Immediate andi $t0, $t1, 7 # t0 = t1&b0111
Shift: left & right logical, arithmetic sllv $t0, $t1, $t2 # t0 = t1<<t2
Immediate sll $t0, $t1, 6 # t0 = t1<<6
Use A Cheat Sheet For These

## Slide 16: Our First Assembly Program
Average Four Numbers
$t5 = ($t0 + $t1 + $t2 + $t3)/4
How do we write this in MIPS Assembly?

## Slide 17: Our First Assembly Program
$t5 = ($t0 + $t1 + $t2 + $t3)/4
add $t5, $t0, $t1 # $t5 = $t0 + $t1
add $t5, $t5, $t2 # $t5 += $t2
add $t5, $t5, $t3 # $t5 += $t3
??? $t5, $t5, 2 # $t5 /= 4
Which Shift do we use?
What assumptions are we making for the inputs?

## Slide 18: Jumping and Branching
Review:
  Jumps change the Program Counter, period.
  Branches check a condition and optionally jump.
  Needs a target location or offset to go to/by
Calculating jump locations by hand is boring
  Let the Assembler do it for us!
  Use Labels

## Slide 19: Jumping / Branching Example
if (a ==b)
a+=3
else
b+=7
c=a+b
A simple example to show case jumping and branching

## Slide 20: Jumping / Branching Example
if (a ==b)
a+=3;
ELSEIF:
b+=7;
ENDIF:
c=a+b
Add labels to indicate our branch / jump targets

## Slide 21: Jumping / Branching Example
if (a !=b) goto ELSEIF
a+=3;
goto ENDIF
ELSEIF:
b+=7;
ENDIF:
c=a+b
Rewrite our if statements
If (x) do y becomes
If (~x) skip y

## Slide 22: Jumping / Branching Example
bne a, b, ELSEIF
a+=3;
j ENDIF
ELSEIF:
b+=7;
ENDIF:
c=a+b
Use specific jump and branch operations

## Slide 23: Jumping / Branching Example
bne a, b, ELSEIF
add a, a, 3
j ENDIF
ELSEIF:
add b, b, 7
ENDIF:
add c, a, b
Translate remaining code
Todo:
  Assign registers to a,b,c
    Human Job
  Calculate offsets
    Assembler Job

## Slide 24: Desk/Board Work
Download MARS
  http://courses.missouristate.edu/kenvollmar/mars/
  http://goo.gl/mOsZ8
Open the environment, start writing assembly
Hint: Work through the process methodically

## Slide 25: Desk/Board Work
Calculate the Sum of integers [0,N]
Calculate Nth Fibonacci Number
Hints:
  N starts in $a0, put answer in $v0
  Use $t0-$t9 as temporary storage
  Set initial conditions with add <dest>, $zero, value
  Comment with #
Bonus:
  Find Square Root (with a Nope Loop? binary search?)
  Find Nth Prime

## Slide 26: Memory Organization
Lets talk to Data Memory!
Viewed as an 1-dimension array
Memory address indexes into array
Byte Addressable:
  8 bits of data per address
0
1
2
3
4
5
6
...
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data

## Slide 27: Memory Organization
Bytes are nice, but our registers are "words"
For MIPS, a word is 32 bits or 4 bytes.
232 bytes with byte addresses from 0 to 232-1
230 words with byte addresses 0, 4, 8, ... 232-4
...
0
4
8
12
32 bits of data
32 bits of data
32 bits of data
32 bits of data
Our registers hold 32 bits of data

## Slide 28: Loads & Stores
Loads & Stores move words between memory and registers
  All operations on registers, but too small to hold all data
  lw $t0, $t1 # $t0 = Memory[$t1]
  sw $t2, $t3 # Memory[$t3] = $t2
Note: lbu & sb load & store bytes
Store
Load
General
Purpose
Registers
t0:
t1:
t2:
t3:
124
723
4
Memory
12:
140:
66

## Slide 29: Word Alignment
Require that objects fall on an address that is a multiple of their size
What are the last two bits of a 32-bit word aligned address?
0 1 2 3
Aligned
Not
Aligned

## Slide 30: Array Example
/* Swap the kth and (k+1)th element of an array */
swap(int v[], int k)
{
int temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}
# Assume v in $a0,
k in $a1
Store
Load
General
Purpose
Registers
a0:
a1:
t0:
t1:
t2:
964
10
Memory
0A12170D
1000
11111111
1004
00000000
1008
FFFFFFFF
1016
0F0F0F0F
1012
FFFFFFFF
1020

## Slide 31: Array Example
/* Swap the kth and (k+1)th element of an array */
swap(int v[], int k)
{
load v[k] into temp0
load v[k+1] into temp1
store temp0 into v[k+1]
store temp1 into v[k]
}
# Assume v in $a0,
k in $a1
Convert array operations in to load / store operations
Why do we need temp1?
Why wasn’t it in the C code?

## Slide 32: Array Example
/* Swap the kth and (k+1)th element of an array */
swap(int v[], int k)
{
address0 = v+k*4
address1 = address0 + 4
load address0 into temp0
load address1 into temp1
store temp0 into address1
store temp1 into address0
}
# Assume v in $a0,
k in $a1
Calculate memory address of v[k] as
v + k * sizeof(int)
v + k * 4

## Slide 33: Array Example
/* Swap the kth and (k+1)th element of an array */
swap(int v[], int k)
{
address0 = k*4
address0+= v
address1 = address0 + 4
load address0 into temp0
load address1 into temp1
store temp0 into address1
store temp1 into address0
}
# Assume v in $a0,
k in $a1
Expand math for calculating address0

## Slide 34: Array Example
/* Swap the kth and (k+1)th element of an array */
swap(int v[], int k)
{
sll address0, k, 2
add address0, address0, v
add address1, address0, 4
lw temp0, (address0)
lw temp1, (address1)
sw temp0, (address1)
sw temp1, (address0)
}
# Assume v in $a0,
k in $a1
Replace with actual instructions
sll – shift left
lw – load word
sw – store word
Todo:
Assign Registers

## Slide 35: Array Example
/* Swap the kth and (k+1)th element of an array */
swap(int v[], int k)
{
sll address0, k, 2
add address0, address0, v
add address1, address0, 4
lw temp0, (address0)
lw temp1, (address1)
sw temp0, (address1)
sw temp1, (address0)
}
# Assume v in $a0,
k in $a1
/* Swap the kth and (k+1)th element of an array */
swap(int v[], int k)
{
int temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}
# Assume v in $a0,
k in $a1

## Slide 36: Next Class
Encoding Machine Instructions
Decoding them in the Decoder

## Slide 37: Remainder of Class
Work on Lab1
Practice Assembly
  Can you reverse an array?
  Can you sort an array?
  How do you multiply in IQ?
    Signed? Unsigned?
  Calculate a Polynomial?
Hint: Prepopulating Arrays
… code code code…
lw $t0, array1($t1)
…snip moar code…
.data
array1
0x12345678 #element0
0x23456789 #element1
…

## Slide 38: IQ in Assembly
Total number of bits is usually:
  Full Word (I+Q=32)
  Half Word (I+Q=16)
Add/Sub are very easy
  Use Integer operations unchanged
Multiplication is mildly tricky
  May require additional operations
Division is a pain

## Slide 39: IQ in Assembly
How do you Multiply?
  Integer Multiplication
  Shift it back in place
  Overflow?
For now, use I8Q8 sign extended
  Top 16 bits are all zero or all one

## Slide 40: IQ in Assembly
Multiply U8Q8 x U8Q8
  Becomes U16Q16
Shift by 8
  Becomes U16Q8 with 16 leading zero bits
And 0x0000FFFF
  Becomes U8Q8 with 16 leading zero bits